## Slide 1
LECTURE 22 | DIGITAL MODULATION FAMILIES
01
CYBER 327 / LECTURE 22
Digital Modulation Families and Constellation Basics
How do bits become a transmitted waveform?
FRIDAY, OCTOBER 23, 2026

## Slide 2
LECTURE 22 | DIGITAL MODULATION FAMILIES
02
START WITH THE NEXT PROBLEM
A radio cannot transmit an abstract 0 or 1
DIGITAL MODULATION ASSIGNS BIT GROUPS TO DISTINGUISHABLE SIGNAL STATES
Notes: The frame may include data, CRC/FEC, and authentication fields.

## Slide 3
LECTURE 22 | DIGITAL MODULATION FAMILIES
02
START WITH THE NEXT PROBLEM
Why Digital Modulation?
GREATER NOISE IMMUNITY
CAN BE COMPRESSED
CAN BE ENCRYPTED
ERROR DETECTION & CORRECTION
Notes: Disadvantages
More complex circuitry
Inherently requires more BW (less efficient in b/s/Hz)

## Slide 4
LECTURE 22 | DIGITAL MODULATION FAMILIES
03
WORK THE EXAMPLE
AM, FM, and PM but digital
Family | What carries the symbol? | Binary example | Flavors
ASK / OOK Amplitude Shift Keying On-off Keying | Carrier amplitude | Off = 0; on = 1 (OOK) | OOK, QAM, 16QAM, 64QAM, 256QAM, etc.
FSK Frequency Shift Keying | Carrier frequency | One tone = 0; another = 1 | BFSK, QFSK, 8FSK, 16FSK, etc.
PSK Phase Shift Keying | Carrier phase | 0 degrees = 1; 180 degrees = 0 | BPSK, QPSK, 8PSK, 16PSK, etc.
Notes: Keying means choosing discrete states.
OOK is a special form of ASK.

## Slide 5
LECTURE 22 | DIGITAL MODULATION FAMILIES
04
MAKE IT VISIBLE
Compare the same 1 0 1 1 message
OOK
1
0
1
1
BFSK
BPSK
Same bits, same symbol slots, different carrier property. Idealized: no pulse shaping.
Notes: Read the four bit slots left to right. OOK changes amplitude; BFSK changes cycles per slot; BPSK reverses carrier phase. The drawing is idealized and editable. It omits pulse shaping and acquisition details; real transmitters must control spectral spreading.

## Slide 6
Example
How many symbols for each modulation if you will transmit 101100?
LECTURE 22 | DIGITAL MODULATION FAMILIES
05
BUILD THE IDEA
A symbol can represent more than one bit
Symbol
One selected signaling state during a symbol interval.
Two states:
0/1 ⟶ one bit per symbol
Four states:
00, 01, 11, and 10 ⟶ two bits per symbol
Modulation | Available choices | Bits per symbol
Binary FSK | 2 frequencies | 1
BPSK | 2 phases | 1
QPSK | 4 phases | 2
16-QAM | 16 amplitude-and-phase combinations | 4
for M possible states
A modulation scheme has 16 possible signal states. How many bits can each symbol represent?
Notes: For fixed-length binary labels and M a power of two, bits/symbol = log2(M). Baud is symbols per second, not necessarily transitions per second: repeated identical symbols need not create a change.

## Slide 7
LECTURE 22 | DIGITAL MODULATION FAMILIES
06
BUILD THE IDEA
I and Q describe a carrier state with two numbers
Plot I horizontally and Q vertically: the result is a constellation.
In-Phase
The amount of the reference carrier
Quadrature
The amount of the carrier shifted by 90o
QPSK symbol | I | Q
00 | +1 | +1
01 | −1 | +1
11 | −1 | −1
10 | +1 | −1
Notes: Use s(t) = I cos(2 pi fc t) - Q sin(2 pi fc t) for this sign convention. Radius gives amplitude; angle gives phase relative to the receiver reference. Receiver mixing and timing recovery estimate I/Q at symbol decision times.

## Slide 8
LECTURE 22 | DIGITAL MODULATION FAMILIES
07
MAKE IT VISIBLE
Constellation is not a spectrum
BPSK: 2 states
I
Q
0
1
QPSK: 4 states
I
Q
00
01
11
10
Bit pair | Phase | I/Q signs
00 | +45 degrees | +I, +Q
01 | +135 degrees | -I, +Q
11 | -135 degrees | -I, -Q
10 | -45 degrees | +I, -Q
TRANSMISSION: 10110001
Notes: BPSK 1 bit/symbol
QPSK 2 bits/symbol
Constellation: which amplitude-and-phase choices represent the bits. The filled dot marks the current choice.
Spectrum: how the transmitted signal’s power is distributed across frequencies over time. This example shows a theoretical spectrum with pulse shaping.

## Slide 9
LECTURE 22 | DIGITAL MODULATION FAMILIES
09
WORK THE EXAMPLE
Baud and bit rate answer different questions
Modulation | Bits per symbol | At 1,000 symbols/s
BPSK: M = 2 | log2(2) = 1 | 1,000 bit/s
QPSK: M = 4 | log2(4) = 2 | 2,000 bit/s
16-QAM: M = 16 | log2(16) = 4 | 4,000 bit/s
bits/symbol
bits/s
symbols/s
Two transmitters operate at 3,000 symbols/s. One uses QPSK; the other uses 16-QAM. Find their bit rates.
A QPSK transmitter must carry a mapped bit rate of 18 kbit/s. What symbol rate is required?
Notes: QPSK: 3,000×2=6,000 bit/s.
- 16-QAM: 3,000×4=12,000 bit/s.
2
Followup: “Would 16-QAM require the same symbol rate? No, half
QPSK: 3,000×2=6,000 bit/s.
- 16-QAM: 3,000×4=12,000 bit/s.
2
𝑅_𝑠=𝑅_𝑏/log_2⁡(𝑀) =18,000/2=9,000
Followup: “Would 16-QAM require the same symbol rate? No, half

## Slide 10
LECTURE 22 | DIGITAL MODULATION FAMILIES
10
BUILD THE IDEA
QAM adds amplitude choices as well as phase
At equal symbol rate, more states carry more mapped bits per second BUT leave less room for errors.

## Slide 11
LECTURE 22 | DIGITAL MODULATION FAMILIES
11
MAKE IT VISIBLE
Noise turns ideal points into clouds
Clean QPSK
I
Q
One ideal point per state
Disturbed QPSK
I
Q
Samples spread around intended states
The receiver measures (-0.7,+0.9). Which bit pair should it choose using the nearest allowed point?
Notes: Additive noise is one cause; timing error, phase error, distortion, and interference can also spread or move points.
01, because the measurement is closest to (-1,+1).

## Slide 12
LECTURE 22 | DIGITAL MODULATION FAMILIES
12
BUILD THE IDEA
Spectral efficiency
Takeaways
More bits per symbol can increase bit/s per Hz without raising symbol rate.
Higher-order modulation is useful only if the receiver can distinguish its states.
Spectral Efficiency (bits/s/Hz)
Spectral efficiency measures how much information we can transmit using a given amount of bandwidth.
Bit rate (bits/s)
Bandwidth (Hz)
A link has:
Bit rate: 24 kbit/s
Code rate: 3/4
BW: 12 kHz
Find:
the information bit rate
gross spectral efficiency
useful spectral efficiency.
Notes: 3R_{info}=24,000×3/4=18,000 bit/s
η_{gross}=24,000/12000=2 bit/s/Hz
η_{useful}=18000/12000=1.5 bit/s/Hz

## Slide 13
LECTURE 22 | DIGITAL MODULATION FAMILIES
15
CHECK UNDERSTANDING
Exit check
A designer changes a link from QPSK to 16-QAM while keeping the same symbol rate and average symbol energy.
What happens to the mapped bit rate?
Why might the receiver make more errors under the same noise conditions?
NEXT: QAM AND BIT ERROR RATE
Notes: It doubles: four bits per symbol instead of two.
The constellation has smaller minimum point spacing, leaving less decision margin.