## Slide 1
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
01
CYBER 327 / LECTURE 16
Filters, Clock Recovery, PLLs, and Synchronization
A receiver must select a channel and recover timing before it can trust symbols.
MONDAY, OCTOBER 12, 2026
Notes: Open with the distinction or case in Slide 2. Preserve the communications model before adding the cybersecurity application. The step may remain outside lock or tracking range even if initial acquisition was possible.

## Slide 2
02
RECALL
The Communication System
Message
Transmitter
Medium
Receiver
Recovered message
Distance α cost, power, size
Must amplify weak signal
Must produce high dv/dt
Must deal with noise

## Slide 3
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
03
COMMUNICATIONS FOUNDATION
Filters keep the signal you want
Filter | V across
Low pass | 
High-pass | 
Band-pass | 
Band-stop | 

## Slide 4
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
03
COMMUNICATIONS FOUNDATION
Filters keep the signal you want
Filter | V across
Low pass | C in RC R in RL C in RLC
High-pass | R in RC L in RL L in RLC
Band-pass | R in RLC
Band-stop | LC in RLC

## Slide 5
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
04
WORKING VOCABULARY
Determine when to read each bit
Clock Recovery
Extraction of symbol timing from a received signal.
Symbol
The physical signal state that represents one or more bits of information.
Bit Interval
= bit rate
Notes: Imagine a digital signal carrying 1,000 bits per second. Each bit lasts 1 ms, but the receiver still needs to locate those bit intervals.

## Slide 6
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
04
WORKING VOCABULARY
Determine when to read each bit
Synchronizing options
Send the clock as a separate signal
  Requires separate channel, more BW
  Common for short-distance communication, where each channel is nearly free
Reference a common signal
  50 Hz, 60 Hz
  GPS clock
  WWV, WWVH – Short wave signal of atomic clock (Coordinated Universal Time)
Derive clock timing from the received data
Use special bits as part of the data stream
#3, 4 together by far the most common for distances over about 15 feet.
Notes: Imagine a digital signal carrying 1,000 bits per second. Each bit lasts 1 ms, but the receiver still needs to locate those bit intervals.

## Slide 7
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
04
WORKING VOCABULARY
Continually Correct the Timing
Phase Locked Loop (PLL)
  A circuit that is used to recover the clock.
  A feedback system.
  It compares an incoming timing reference with a local oscillator and adjusts the oscillator to stay aligned.
Notes: Imagine a digital signal carrying 1,000 bits per second. Each bit lasts 1 ms, but the receiver still needs to locate those bit intervals.

## Slide 8
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
04
WORKING VOCABULARY
Continually Correct the Timing
Capture range
  The frequencies at which a PLL can initially synchronize with an incoming signal.
  The frequencies over which a PLL can remain synchronized after it has already locked.
Lock range

## Slide 9
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
04
WORKING VOCABULARY
Types of Encoding
  Can you recover the timing if you transmit a lot of zeroes/ones?

## Slide 10
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
04
WORKING VOCABULARY
Continually Correct the Timing
  Encode the data so that long sequences without transitions are avoided.
Run-Length Limiting (RLL)

## Slide 11
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
08
APPLICATION
Cybersecurity follows the physical behavior
Network receivers
An attacker does not need to access the message. They can disturb the timing to misread bits, reject message or lose sync.

## Slide 12
LECTURE 16 | FILTERS CLOCK RECOVERY PLLS
10
BRIDGE FORWARD
Exit check
How can a valid-looking signal still fail if timing is wrong?
NEXT: RECEIVER ARCHITECTURE, SENSITIVITY, AND SE