## Slide 1
LECTURE 19 | ALIASING FALSE TELEMETRY AND
01
CYBER 327 / LECTURE 19
Aliasing, False Telemetry, and Sensor Spoofing
A valid-looking digital value can misrepresent the physical input.
FRIDAY, OCTOBER 16, 2026

## Slide 2
LECTURE 19 | ALIASING FALSE TELEMETRY AND
02
FROM CONCEPT TO EVIDENCE
Sampling can create a false picture
Aliasing
a sampled signal becomes distorted because the sampling rate is too low to accurately capture the original data.
https://so-okada.github.io/math_teaching_materials/sampling_theorem_aliasing.html
Notes: Use the three cards as an advance organizer. Ask students what prior-week idea each card depends on.

## Slide 3
LECTURE 19 | ALIASING FALSE TELEMETRY AND
05
QUANTITATIVE MODEL
Nyquist-Shannon Sampling Theorem
An analog signal can be perfectly reconstructed without loss of information if it is sampled greater than twice the highest frequency component.
Alias location
If not, aliasing will occur!
24 Hz Camera, 24 Hz Water
24 Hz Camera, 25 Hz Water
24 Hz Camera, 23 Hz Water
Actual Input | Sampling Rate | Apparent frequency
200 Hz | 2000 samples/s | 200 hz
1800 Hz | 2000 samples/s | 200 hz
1800 Hz | 5000 samples/s | 1800 Hz
Notes: It should be greater than!
If equal, its 0

## Slide 4
LECTURE 19 | ALIASING FALSE TELEMETRY AND
08
APPLICATION,
Cybersecurity follows the physical behavior
A genuine 200 Hz input activates it correctly.
But a 1,800 Hz input sampled at 2,000 samples/s can also appear to be 200 Hz and activate it incorrectly.
How can you protect against this?
Notes: Increase the sampling rate so the 1,800 Hz signal is represented correctly.
- Filter unwanted frequencies before the ADC so less interference reaches it.

## Slide 5
LECTURE 19 | ALIASING FALSE TELEMETRY AND
10
BRIDGE FORWARD
Exit check
Are there other ways to correct misrepresentations?
NEXT: ERROR DETECTION AND CORRECTION FUNDAMENTAL
Notes: Use the response to open the next meeting. Practice-case resolution: The input is above Nyquist and aliases to an indistinguishable sampled sequence.