## Slide 1
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
01
CYBER 327 / LECTURE 24
OFDM, Spread Spectrum, and Shannon Revisited
How should we organize a waveform when the channel causes problems?
WEDNESDAY, OCTOBER 28, 2026

## Slide 2
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
02
FROM MEASURED BER TO WAVEFORM DESIGN
Review on QPSK/QAM

## Slide 3
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
03
OFDM = ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
OFDM sends symbol groups in parallel
All eight subcarriers are simultaneous during one useful OFDM interval. The receiver separates them, then makes the constellation decisions.
Goal
Spread the transmission across multiple subcarriers simultaneously

## Slide 4
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
06
MULTIPATH = DIFFERENT PATHS AND ARRIVAL TIMES; CP = CYCLIC PREFIX
A cyclic prefix gives delayed copies room
Multipath
A signal reaches a receiver through more than one path

## Slide 5
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
06
MULTIPATH = DIFFERENT PATHS AND ARRIVAL TIMES; CP = CYCLIC PREFIX
A cyclic prefix gives delayed copies room
The cyclic prefix must cover the echo/delays
CP: 25 us
Useful block: 100 us
Tail: 25 us
Copy the same samples
Useful interval (the symbol)

## Slide 6
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
05
DEFINE T_U BEFORE TAKING ITS RECIPROCAL
Longer useful intervals mean closer spacing
Spacing
Useful interval u | Calculation | Subcarrier spacing
100 us | 1 / (100 x 10^-6 s) | 10 kHz
50 us | 1 / (50 x 10^-6 s) | 20 kHz
 | Calculation | Subcarrier spacing
100 us | 1 / (100 x 10^-6 s) | 10 kHz
50 us | 1 / (50 x 10^-6 s) | 20 kHz
Useful Interval
Subcarrrier spacing | Calculation | Useful interval u
25 kHz | 1 / (25000) | 40 us
5 kHz | 1 / (5000) | 200 us
Subcarrrier spacing | Calculation | 
25 kHz | 1 / (25000) | 40 us
5 kHz | 1 / (5000) | 200 us

## Slide 7
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
07
SIMPLIFIED EXAMPLE: ALL EIGHT SUBCARRIERS CARRY DATA; NO OTHER OVERHEAD
The cost of using cyclic prefix
I designed an OFDM link with 8 QPSK data subcarriers. I measured delays in my medium to be 15us, so I want my prefix to be 25 us. If I want Tu to be 100us, what is my bitrate?
Quantity | Calculation | Result
Adjacent spacing |  | 10 kHz
Complete block/symbol rate |  | 8,000 symbols/s
Mapped bit rate |  | 128 kbit/s
Quantity | Calculation | Result
Adjacent spacing |  | 10 kHz
Complete block/symbol rate |  | 8,000 symbols/s
Mapped bit rate |  | 128 kbit/s

## Slide 8
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
07
SIMPLIFIED EXAMPLE: ALL EIGHT SUBCARRIERS CARRY DATA; NO OTHER OVERHEAD
Comparing with QPSK
Quantity | QPSK + OFDM | Single-carrier QPSK | Single-carrier QPSK
Useful time to send 16 bits | 100 µs | 800 µs | 100 µs
(Useful) Baud Rate | 10 k baud | 10 k baud | 80,000 baud
Data carriers | 8 simultaneously | 1 | 1
Useful duration of each QPSK symbol | 100 µs per subcarrier | 100 µs | 100µs/8symbols =12.5 µs
How 16 bits are sent | 8 QPSK symbols simultaneously | 8 QPSK symbols sequentially | 8 QPSK symbols sequentially
Prefix included in this comparison | 25 µs per block | None | None
Total time for 16 bits | 125 µs | 800 µs | 100 µs
Bit rate | 128 kbit/s | 20 kbit/s | 160 kbit/s

## Slide 9
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
09
FHSS = FREQUENCY-HOPPING SPREAD SPECTRUM; CONCEPTUAL SEQUENCE
Frequency Hopping Spread Spectrum (FHSS)
Goal
Spread the transmission by hopping across multiple frequencies over time

## Slide 10
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
10
DSSS = DIRECT-SEQUENCE SPREAD SPECTRUM; A SHORT TEACHING CODE
Direct Sequence Spread Spectrum (DSSS)
Goal
Spread the transmission to a wider band continuously

## Slide 11
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
11
ILLUSTRATIVE IDEAL CHIPS; REAL RECEPTION NEEDS SYNCHRONIZATION AND NOISY-SAMPLE DECISIONS
Matched despreading recovers the data
Data bit | Repeated bit | XOR sequence | Transmitted chips
1 | 1111111 | 1011001 | 0100110
0 | 0000000 | 1011001 | 1011001
1 | 1111111 | 1011001 | 0100110
Transmit: 101 Chip: 1011001
Received chips | XOR sequence | Despread result | Majority decision
0110110 | 1011001 | 1101111 | Six ones → 1
1111101 | 1011001 | 0100100 | Five zeros → 0
0100100 | 1011001 | 1111101 | Six ones → 1

## Slide 12
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
12
THESE MECHANISMS CAN BE COMBINED; NONE IS AN AUTHENTICATION CHECK
Choose the mechanism for the problem
Method | Good when you have | What to watch out for
OFDM + CP | Multipath/delayed reflected copies | Prefix time, synchronization
FHSS | Narrow band interference | Hop timing and channel sequence
DSSS | Narrow band interference Weak signal | Wider band, code alignment

## Slide 13
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
13
IDEAL BAND-LIMITED CHANNEL WITH ADDITIVE WHITE GAUSSIAN NOISE
Shannon still bounds the information rate
Information rate | What Shannon says
300 kbit/s | Arbitrarily low error probability is theoretically achievable with suitable coding
500 kbit/s | Arbitrarily low error probability is impossible under the same channel conditions
For a Shannon Capacity of 400 kbit/s,
“Reliable communication is impossible”
you cannot sustain that information rate and eliminate errors. To improve reliability, you must reduce the information rate or improve the channel’s bandwidth or SNR.

## Slide 14
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
16
ASSUME CORRECT TIMING, A STABLE CHANNEL AND NO ADDITIONAL OVERHEAD
Practice
We have QPSK link with:
6 subcarriers
Tu = 50us
TCP = 10 us
RC =3/4
Find:
the subcarrier spacing,
the bit rate,
the information-bit rate, and
whether an 8 us delay fits within the prefix.
A channel has 100 kHz bandwidth and 10dB SNR.
A design claims 400 kbits/s of information.
A second design targets 250 kbits/s of information.
Can the channel support both designs?
dB
Notes: Yes it fits the prefix
Design 1 is impossible
Design 2 is possible

## Slide 15
LECTURE 24 | OFDM SPREAD SPECTRUM AND SHA
18
CHECK UNDERSTANDING
Exit check
What if we still fail?
NEXT: PULSES, TIMING AND EYE PATTERNS