## Slide 1
LECTURE 20 | ERROR DETECTION AND CORRECTI
01
CYBER 327 / LECTURE 20
Error Detection and Correction Fundamentals
The sensor sent one message. How can we notice or repair changed bits?
MONDAY, OCTOBER 19, 2026

## Slide 2
LECTURE 20 | ERROR DETECTION AND CORRECTI
02
PRACTICE RECAP
Practice Problems
ADC code
An ideal 8-bit ADC measures voltages from 0 to 10.00 V.
How many possible codes does it have?
Calculate its ideal voltage step.
Approximately what code corresponds to 2.62 V?
PLL recovery
A PLL is centered at 10.0 kHz. Its capture range is ±200 Hz, and its lock range is ±600 Hz.
The PLL starts unlocked. The input is 10.4 kHz. Is that input within its capture range?
The PLL is already locked at 10.2 kHz, and the input slowly drifts to 10.7 kHz. Is that input still within its stated lock range?
Sensitivity
A receiver needs at least −95 dBm at its input to meet its stated performance target. The received signal is −78 dBm.
Calculate the sensitivity margin.
An attenuator reduces the received signal by 20 dB. Is the signal still above the sensitivity threshold?
Notes: PLL
  No
  No
Sensitivity
  17 dB
  -98, no
ADC
  256
  39mV
  67

## Slide 3
LECTURE 20 | ERROR DETECTION AND CORRECTI
02
PRACTICE RECAP
Practice Problems
Sampling Interval
A sampler takes 4,000 samples per second. Calculate the time between samples.
Alarm
A detector for an alarm samples at 2,000 samples/s. It has activated on a sinewave of 4600 Hz.
Predict the apparent frequency. Should the alarm activate?
Leave the input unchanged and increase sampling to 10,000 samples/s. Predict the apparent frequency and alarm state.
PCM
A single-channel PCM system takes 8,000 samples each second and represents each sample with 8 bits.
Calculate the bit rate.
Notes: 600 Hz, No
4600 Hz
64kbits/s
1/4000

## Slide 4
02
SYSTEM GOAL
Components of all Communication Systems
Message
Transmitter
Medium
Receiver
Recovered message
EVERY BLOCK TRANSFORMS, TRANSPORTS, OR INTERPRETS A PHYSICAL SIGNAL
Notes: a waveform has both a time-domain appearance and a frequency-domain structure
signals compete with noise so we consider bandwidth and SNR (Shannon) AM changes carrier amplitude; FM changes instantaneous frequency.
Receiver: Clock recovery, PLLs. Sensitivity
Sampling, Aliasing

## Slide 5
LECTURE 20 | ERROR DETECTION AND CORRECTI
02
START WITH A PROBLEM
How do I know that the bits changed?
Redundancy
Extra information beyond the original data
Error control
  Error detection
    parity, checksum, CRC
  Error correction
    ARQ, FEC, Interleaving

## Slide 6
LECTURE 20 | ERROR DETECTION AND CORRECTI
04
MAKE IT VISIBLE
Parity Bits
Sent
1
0
1
1
1
4 ones: even
One bit changed
1
0
0
1
1
3 ones: FAIL
Two bits changed
1
1
0
1
1
4 ones: PASS
Data | Parity
Set Even or Odd Parity
Even parity: Data plus parity must contain an even number of 1s
Odd parity: Data plus parity must contain an odd number of 1s
Notes: Can parity locate where the error occurred? No
What are the problems with this?

## Slide 7
LECTURE 20 | ERROR DETECTION AND CORRECTI
04
MAKE IT VISIBLE
Parity Bits
Character | ASCII bits | Number of ones | Added parity bit
S | 01010011 | 4 | 0
A | 01000001 | 2 | 0
F | 01000110 | 3 | 1
E | 01000101 | 3 | 1
Transmission: 010100110010000010010001101010001011
Received: 010100110010000010010001101010001001
Received: 010100110010000010010001101010001101
PASS
FAIL
Notes: Can parity locate where the error occurred? No
What are the problems with this?

## Slide 8
LECTURE 20 | ERROR DETECTION AND CORRECTI
04
MAKE IT VISIBLE
Checksum
Transmission: 01010011 01000001 01000110 01000101 00011111
Received: 01010011 01000001 01000110 01000100 00011111
Received: 01010011 01000001 01000111 01000100 00011111
PASS
FAIL
Character | S | A | F | E | Total
Numerical code | 83 | 65 | 70 | 69 | 287
For an 8-bit checksum, mod by 256:
= 00011111

## Slide 9
LECTURE 20 | ERROR DETECTION AND CORRECTI
04
MAKE IT VISIBLE
Cyclic Redundancy Check (CRC)
Transmission: 01010011 01000001 01000110 01000101 11010010
      Received:
      Calculated:
Runs the message’s bits through an agreed calculation to produce a short check value.
S A F E
0x53 0x41 0x46 0x45 0xD2
S A F E
0x53 0x41 0x46 0x44 0xD2
0x53 0x41 0x46 0x44 0xD5
FAIL
8-bit CRC

## Slide 10
LECTURE 20 | ERROR DETECTION AND CORRECTI
03
ERROR CHECKS
Send extra information so errors leave a clue
Check | Chance of missing a corrupted message
One parity bit | About 1 in 2
8-bit additive checksum | About 1 in 256
8-bit CRC | About 1 in 256
16-bit additive checksum | About 1 in 65,536
16-bit CRC | About 1 in 65,536
32-bit additive checksum | About 1 in 4.3 billion
32-bit CRC | About 1 in 4.3 billion
Equal numbers ≠ Equal Protection
Error pattern | Simple 8-bit additive checksum | 8-bit CRC
One data bit flips | Always detects | Always detects
One byte increases by 1; another decreases by 1 | Always misses | Detects many such changes; depends on positions and CRC
Two different data bytes swap positions | Always misses | Detects many swaps; depends on data and CRC
Burst spanning up to 8 bits | Can miss some | Always detects*
Right table assumes uniformly random errors

## Slide 11
LECTURE 20 | ERROR DETECTION AND CORRECTI
09
BUILD THE IDEA
A failed check gives us two recovery choices
Request another copy: automatic repeat request (ARQ). This costs time and requires a return path.
Add enough structured redundancy to repair some errors: forward error correction (FEC).
1
2
CRC Transmission: 01010011 01000001 01000110 01000101 11010010
FEC Transmission: 000 111 000 111 000 000 111 111 000 111 000 000 000 000 000 111 000 111 000 000 000 111 111 000 000 111 000 000 000 111 000 111 000 000 000 111 111 111 111 111
Simplest implementation of FEC: majority correction:
1 transmits as 111
What are the disadvantages for this specific FEC?
Notes: the checksum/CRC is calculated before the FEC bits are added.
Add FEC to [SAFE | CRC]
3x the transmitted bits
If non-random errors (burst) can still give errors

## Slide 12
LECTURE 20 | ERROR DETECTION AND CORRECTI
09
BUILD THE IDEA
Error Correcting Code (ECC): Block Parity
Parity in 2 dimensions
Arrange the data in a grid, then add parity bits for each row and each column
What could go wrong with this?
Data |  |  |  | Parity
1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
0 | 0 | 0 | 0 | 
Assume even parity. Which bit(s) could be erroneous?
Data |  |  |  | Parity
1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 
1 error
2 errors
Notes: 2 errors: detected but location ambiguous

## Slide 13
LECTURE 20 | ERROR DETECTION AND CORRECTI
12
BUILD THE IDEA
Bursts & Interleaving
Interleaving
sends pieces of different codewords in alternating order.
Spreads burst damage so ECC can work well
Random errors are scattered, but a burst damages a nearby run of transmitted bits.
Burst Error
Notes: After deinterleaving, a code capable of one correction per word can handle this example.

## Slide 14
LECTURE 20 | ERROR DETECTION AND CORRECTI
13
WORK THE EXAMPLE
Reliability has a rate and delay cost
Storage Tech | Interpretation
HDD | 1 unrecoverable sector per bits transferred
SSD | 1 unrecoverable sector per bits read
USB Flash | 1 bit error per bits read.
LTO-9 tape | 1 uncorrectable error event per user bits
Storage Tech | Interpretation
HDD | 
SSD | 
USB Flash | 
LTO-9 tape | 
If reading at 100MB/s:
bits: 1 every 14.5 days
bits: 1 every 4,000 years
Code Rate
How much of the packet is data?
Information Bit Rate
What rate remains?
CRC Error Probability
the probability that a corrupted frame passes its CRC check
r = CRC bits
Notes: If 8 data over 12 coded bits:
30 kbit/s
Rc = 2/3
Rinfo =20 kbit/s

## Slide 15
LECTURE 20 | ERROR DETECTION AND CORRECTI
15
CHECK UNDERSTANDING
Explain the next step
The CRC passes. What do we still not know?
Name one error the chosen code can detect, one cost of redundancy, and one unsupported trust claim.
NEXT: WHO AUTHORIZED THE MESSAGE?