## Slide 1
LECTURE 02 | FOUNDATIONS II
01
CYBER 327 / LECTURE 02
Electrical Foundations II
Ohm’s Law and Series Circuits
SEP 04, 2026
Notes: Connect directly to Wednesday and the lab that follows. Keep arithmetic purposeful and measurement-centered.

## Slide 2
LECTURE 02 | FOUNDATIONS II
15
FROM LAST LECTURE
Recap
Why does a circuit need a complete loop?
Can’t it be just one line?

## Slide 3
LECTURE 02 | FOUNDATIONS II
15
FROM LAST LECTURE
A Thought Experiment

## Slide 4
LECTURE 02 | FOUNDATIONS II
03
FOUNDATION RECAP
Electronic Terms
Term | Units | Unit Abbrev | Symbol
Voltage | Volts | V | E/V
Current | Amperes | A | I
Resistance | Ohms | Ω | R
Power | Watts | W | P
Frequency | Hertz | Hz | f

## Slide 5
LECTURE 02 | FOUNDATIONS II
04
UNITS AND PREFIXES
ENGINEERING NOTATION
Prefix | Symbol | Multiplier | Prefix | Symbol | Multiplier
milli | m | 10-3 | kilo | k | 103
micro | µ | 10-6 | Mega | M(illion) | 106
nano | n(ine) | 10-9 | Giga | G | 109
pico | p | 10-12 | Tera | T(welve) | 1012
0.00900 V
[1-999] [prefix] [unit]
0.00001383 A
2 430 000 000 W
6.7 k Ω
Convert:

## Slide 6
LECTURE 02 | FOUNDATIONS II
05
CORE RELATIONSHIPS
Ohm’s Law
Voltage across a resistance equals current through it times resistance.
For a fixed voltage, more total resistance means ___ current.
For a fixed resistance, more voltage means ___ current.

## Slide 7
LECTURE 02 | FOUNDATIONS II
05
CORE RELATIONSHIPS
Ohm’s Law

## Slide 8
LECTURE 02 | FOUNDATIONS II
05
CORE RELATIONSHIPS
Power Formula
Remember:

## Slide 9
LECTURE 02 | FOUNDATIONS II
06
THE FIRST TOPOLOGY
THE CIRCUIT
Remember:
Let:
KIRCHOFF’S VOLTAGE LAW
The total voltage around any closed loop or path in a circuit must add up to zero.
The voltage across the source should be equal to the voltage across all the loads
What is the current passing through R, IR?
What is the voltage drop across R, VR?
What is the power dissipated by R?
SOURCE
LOAD
Notes: Have students trace the path aloud. Use conventional current direction only; avoid electron-flow digression.

## Slide 10
LECTURE 02 | FOUNDATIONS II
06
THE FIRST TOPOLOGY
THE SERIES CIRCUIT
Remember:
Let:
What is the total resistance?
What is the current passing through RTOTAL, IR?
What is the voltage drop across R1, VR1?
What is the voltage drop across R2, VR2?
NODE A
NODE B
NODE C
GROUND

## Slide 11
LECTURE 02 | FOUNDATIONS II
06
THE FIRST TOPOLOGY
THE SERIES CIRCUIT
Remember:
Let:
KIRCHOFF’S CURRENT LAW
The total current entering a node must equal the total current leaving that same node.
The current across series components are equal
What is the total resistance?
What is the current passing through RTOTAL, IR?
What is the voltage drop across R1, VR1?
What is the voltage drop across R2, VR2?
NODE A
NODE B
NODE C
GROUND

## Slide 12
LECTURE 02 | FOUNDATIONS II
06
THE FIRST TOPOLOGY
THE SERIES CIRCUIT
Remember:
Let:
What is the total resistance?
What is the current passing through RTOTAL, IR?
What is the voltage drop across R1, VR1?
What is the voltage drop across R2, VR2?
NODE A
NODE B
NODE C
GROUND

## Slide 13
LECTURE 02 | FOUNDATIONS II
06
THE FIRST TOPOLOGY
THE VOLTAGE DIVIDER
Let:
What is the total resistance?
What is the current passing through RTOTAL, IR?
What is the voltage drop across R1, VR1?
What is the voltage drop across R2, VR2?
NODE A
NODE B
NODE C
GROUND

## Slide 14
LECTURE 02 | FOUNDATIONS II
06
THE FIRST TOPOLOGY
THE VOLTAGE DIVIDER
Let:
What is the voltage of Node A, VA?
What is the voltage of Node B, VB?
What is the voltage of Node C, VC?
NODE A
NODE B
NODE C
GROUND

## Slide 15
LECTURE 02 | FOUNDATIONS II
09
MEASUREMENT SAFETY
HOW DOES ONE GET THE MEASUREMENT?
Mode | Connection
Voltage | Across two points (parallel)
Resistance | Across isolated component/path
Current | Open path; insert meter in series
What if my measurements are off?

## Slide 16
LECTURE 02 | FOUNDATIONS II
09
MEASUREMENT SAFETY
HOW DOES ONE GET THE MEASUREMENT?
Mode | Connection
Voltage | Across two points (parallel)
Resistance | Across isolated component/path
Current | Open path; insert meter in series
What if my measurements are off?

## Slide 17
LECTURE 02 | FOUNDATIONS II
09
MEASUREMENT SAFETY
HOW DOES ONE GET THE MEASUREMENT?
Mode | Connection
Voltage | Across two points (parallel)
Resistance | Across isolated component/path
Current | Open path; insert meter in series
What if my measurements are off?

## Slide 18
LECTURE 02 | FOUNDATIONS II
10
TOLERANCE AND UNCERTAINTY
What if my measurements are off?
Component tolerance
A 5% resistor may legitimately differ from its printed nominal value.
Instrument limits
Resolution, accuracy, lead resistance, and reference choice affect measured values.
Meaningful deviation
A fault claim needs a stable pattern larger than plausible variation and consistent with circuit behavior.
COMPARE AGAINST A MEASURED BASELINE

## Slide 19
LECTURE 02 | FOUNDATIONS II
06
THE FIRST TOPOLOGY
CHANGES TO THE CIRCUIT
Your friend says:
You measure:
NODE A
NODE B
NODE C
GROUND
Does this check out?

## Slide 20
LECTURE 02 | FOUNDATIONS II
15
READY FOR THE LAB?
Exit check
A 5.00 V source drives 5.00 kohm total. What current should flow?
How should you connect the ammeter to measure the current?
NEXT: PARALLEL CIRCUITS & POWER