## Slide 1
LECTURE 06 | TRANSFORMERS + ISOLATION
01
CYBER 327 / LECTURE 06
Transformers, Isolation, and Coupling
Controlled magnetic transfer creates useful links and imperfect boundaries.
SEP 16, 2026

## Slide 2
LECTURE 06 | TRANSFORMERS + ISOLATION
02
MENTAL MODEL
A transformer is controlled magnetic coupling
Energy transfers through a changing magnetic field.
NO CHANGING FLUX -> NO IDEAL TRANSFORMER ACTION

## Slide 3
LECTURE 06 | TRANSFORMERS + ISOLATION
02
MENTAL MODEL
A transformer is controlled magnetic coupling
Energy transfers through a changing magnetic field.
NO CHANGING FLUX -> NO IDEAL TRANSFORMER ACTION

## Slide 4
LECTURE 06 | TRANSFORMERS + ISOLATION
03
CORE RELATIONSHIP
Turns ratio sets ideal voltage ratio
Voltage follows the turns ratio.
Current ratio is inverse for an ideal transformer.
Real output is lower because of loss.
STEP-UP VOLTAGE MEANS STEP-DOWN CURRENT CAPABILITY

## Slide 5
LECTURE 06 | TRANSFORMERS + ISOLATION
02
MENTAL MODEL
Why transformers?
Step voltage up (and current down)
Step voltage down (and current up)
Provide DC isolation (block DC)
Provide impedance matching
AC IS EFFICIENT BECAUSE OF TRANSFORMERS
REMEMBER

## Slide 6
LECTURE 06 | TRANSFORMERS + ISOLATION
09
MATCHING INTUITION
Impedance can be reflected across a transformer
2:1 TURNS = 4:1 IMPEDANCE
Impedance Matching
Making source and load work well together
Amplifier
6Ω
Speaker
Transformer
The amplifier works best if it sees 600 Ω. What should be the output transformer?

## Slide 7
LECTURE 06 | TRANSFORMERS + ISOLATION
04
PREDICT BEFORE MEASURING
Ratio example

## Slide 8
LECTURE 06 | TRANSFORMERS + ISOLATION
05
NON-IDEAL BEHAVIOR
Real inductors and transformers have limits
Loss
Winding resistance and core loss turn some stored or transferred energy into heat.
Frequency limits
Parasitic capacitance, self-resonance, and core saturation limit ideal reactance and transfer.
Ratings
Current, voltage, frequency, insulation, and temperature limits must all be respected.
Blocks
Direct DC continuity and many ground-loop currents.
Passes
Changing signals and power within the transformer's bandwidth.
May still couple
Capacitance, leakage flux, common-mode energy, or unsafe insulation failure.
Notes: Connect back to Lecture 5: X_L = 2 pi f L is an ideal model

## Slide 9
LECTURE 06 | TRANSFORMERS + ISOLATION
07
WHERE IS THE CURRENT TRYING TO GO?
Useful current vs. unwanted current paths
Mode | Where measured | Typical concern
Differential | Between two signal conductors | Desired information or line imbalance
Common mode | Both conductors relative to a shared reference | Leakage, ground current, emissions
Ground loop | Multiple return paths at different potential | Hum, error, unsafe current
Isolation barrier | No intended conductive return | Barrier rating and parasitic coupling
Coupling can bypass intended wiring
Magnetic coupling: changing current in one loop produces a changing magnetic field that reaches another loop
Capacitive coupling: changing voltage transfers energy through the small unintended capacitance between conductors.
Conducted coupling: signals travel through a shared ground, supply, or return path.

## Slide 10
LECTURE 06 | TRANSFORMERS + ISOLATION
12
BEFORE FRIDAY
Exit check
A transformer has twice as many secondary turns as primary turns. What happens to ideal voltage?
NEXT: EMI + CONTAINMENT
Notes: Expected voltage doubles; ideal current capability halves.