## Slide 1
LECTURE 09 | RESONANCE + FILTERING
01
CYBER 327 / LECTURE 09
Resonance, Selectivity, and Filtering
Measure which frequencies a channel favors, attenuates, and cannot separate.
SEP 23, 2026
Notes: Turn the RLC model into measurable channel selectivity. Keep dB out of this lecture; use amplitude ratios and the 0.707 half-power criterion.

## Slide 2
LECTURE 09 | RESONANCE + FILTERING
02
OPENING PROBLEM
A receiver should not treat every frequency equally
Desired
A known channel occupies a limited frequency region.
Undesirable
Noise and interference may exist above, below, or inside that region.
Notes: Ask whether a filter can distinguish two sources at exactly the same frequency. No: frequency selectivity alone cannot separate coincident signals.

## Slide 3
LECTURE 09 | RESONANCE + FILTERING
02
OPENING PROBLEM
A receiver should not treat every frequency equally
Desired
A known channel occupies a limited frequency region.
Undesirable
Noise and interference may exist above, below, or inside that region.
Notes: Ask whether a filter can distinguish two sources at exactly the same frequency. No: frequency selectivity alone cannot separate coincident signals.

## Slide 4
LECTURE 09 | RESONANCE + FILTERING
02
OPENING PROBLEM
A receiver should not treat every frequency equally
Desired
A known channel occupies a limited frequency region.
Undesirable
Noise and interference may exist above, below, or inside that region.
Notes: Ask whether a filter can distinguish two sources at exactly the same frequency. No: frequency selectivity alone cannot separate coincident signals.

## Slide 5
LECTURE 09 | RESONANCE + FILTERING
02
RECALL
Filters
RC Circuit
RL Circuit
HIGHER F = HIGHER I
HIGHER F = LOWER I
Notes: Ask whether a filter can distinguish two sources at exactly the same frequency. No: frequency selectivity alone cannot separate coincident signals.

## Slide 6
LECTURE 09 | RESONANCE + FILTERING
02
RECALL
Filters
RC Circuit
RL Circuit
HIGH PASS FILTER
LOW PASS FILTER
Accepts higher frequencies
Accepts lower frequencies
Notes: Ask whether a filter can distinguish two sources at exactly the same frequency. No: frequency selectivity alone cannot separate coincident signals.

## Slide 7
LECTURE 09 | RESONANCE + FILTERING
02
BUT
Filters depend on where you look
RC Circuit
RL Circuit
HIGH PASS FILTER
LOW PASS FILTER
+
V
-
+
V
-
Look at V across R
Notes: Ask whether a filter can distinguish two sources at exactly the same frequency. No: frequency selectivity alone cannot separate coincident signals.

## Slide 8
LECTURE 09 | RESONANCE + FILTERING
02
BUT
Filters depend on where you look
RC Circuit
RL Circuit
LOW PASS FILTER
HIGH PASS FILTER
+ V -
Look at V across L/C
+ V -
Notes: Ask whether a filter can distinguish two sources at exactly the same frequency. No: frequency selectivity alone cannot separate coincident signals.

## Slide 9
LECTURE 09 | RESONANCE + FILTERING
02
BUT
Filters depend on where you look
RC Circuit
RL Circuit
CUTOFF FREQUENCY
+ V -
+ V -
Frequency where it breaks even
Notes: Ask whether a filter can distinguish two sources at exactly the same frequency. No: frequency selectivity alone cannot separate coincident signals.

## Slide 10
LECTURE 09 | RESONANCE + FILTERING
03
RESONANT FREQUENCY
Series resonance occurs when reactances balance
Inductive and capacitive reactance magnitudes match.
Z at f0 is about R
Series current reaches its maximum.
AT RESONANCE: NET REACTANCE = 0
Resonant Frequency
Notes: Images: https://www.ebay.com/itm/406656200825 https://www.voltraware.com/magnetic-resonance-technology-wireless-charging/

## Slide 11
LECTURE 09 | RESONANCE + FILTERING
04
RLC IN RESONANCE
The band-pass filter
CURRENT IS MAXIMUM AT RESONANCE

## Slide 12
LECTURE 09 | RESONANCE + FILTERING
04
RLC IN RESONANCE
The band-pass filter
V ACROSS C
V ACROSS L
V ACROSS R

## Slide 13
LECTURE 09 | RESONANCE + FILTERING
06
HALF-POWER CRITERION
Bandwidth needs a stated boundary
Amplitude at half power for equal impedance. (-3dB point)
Width between the two crossing frequencies.
Quality Factor. Sharpness of the measured response.
Notes: https://www.allaboutcircuits.com/textbook/alternating-current/chpt-6/q-and-bandwidth-resonant-circuit/

## Slide 14
LECTURE 09 | RESONANCE + FILTERING
07
TRADEOFF
Q describes selectivity, not quality in general
Higher Q
Narrower bandwidth and stronger discrimination near f0.
Lower Q
Broader response and less sensitivity to tuning error.
System tradeoff
A very narrow filter may reject a drifting or wideband desired signal.

## Slide 15
LECTURE 09 | RESONANCE + FILTERING
08
RESPONSE CATEGORIES
Four basic filters answer different needs
Filter | Primarily passes | Primarily attenuates | Example
Low-pass | Below cutoff | Above cutoff | Remove high-frequency noise
High-pass | Above cutoff | Below cutoff | Block DC or slow drift
Band-pass | Selected band | Outside the band | Select one channel
Band-stop/Band-reject | Outside a rejected band | Selected band | Suppress a narrow interferer
Notes: How do you get a band reject filter?

## Slide 16
LECTURE 09 | RESONANCE + FILTERING
14
SELECTIVITY CLAIM
Exit check
End of prologue
Welcome to Communication Systems
NEXT: MESSAGES, SIGNALS, CARRIERS AND CHANNELS