## Slide 1
LECTURE 18 | PULSE MODULATION PCM ADCS AN
01
CYBER 327 / LECTURE 18
Pulse Modulation, PCM, ADCs, and DACs
Sampling and quantization turn analog evidence into finite digital codes.
WEDNESDAY, OCTOBER 14, 2026
Notes: Open with the distinction or case in Slide 2. Preserve the communications model before adding the cybersecurity application. One ideal step is about 19.5 mV; values within a step map to the same code.

## Slide 2
LECTURE 18 | PULSE MODULATION PCM ADCS AN
02
FROM CONCEPT TO EVIDENCE
Today's learning route
Foundation
Pulse modulation and PCM workflow
Model
Sampling rate, quantization, resolution, step size, and reconstruction
Evidence
ADC and DAC practical behavior
Notes: Use the three cards as an advance organizer. Ask students what prior-week idea each card depends on.

## Slide 3
LECTURE 18 | PULSE MODULATION PCM ADCS AN
03
COMMUNICATIONS FOUNDATION
Core ideas to connect
# | Topic | Student action
1 | Pulse modulation and PCM workflow | Explain, predict, or measure
2 | Sampling rate, quantization, resolution, step size, and reconstruction | Explain, predict, or measure
3 | ADC and DAC practical behavior | Explain, predict, or measure
4 | Quantization error and distortion | Explain, predict, or measure
Notes: Do not present these as isolated vocabulary. For each row, obtain a prediction, example, or measurable consequence.

## Slide 4
LECTURE 18 | PULSE MODULATION PCM ADCS AN
04
WORKING VOCABULARY
Terms must be tied to observations
Term | Operational meaning
ADC | Device that converts an analog input into a digital code.
DAC | Device that converts a digital code into an analog output.
aliasing | False frequency representation caused by sampling too slowly.
Notes: Require students to use each term in a sentence that names a signal, channel, instrument, or decision.

## Slide 5
LECTURE 18 | PULSE MODULATION PCM ADCS AN
05
QUANTITATIVE MODEL
Relationships support testable predictions
levels = 2^N
Quantization levels
delta = full scale / 2^N
Ideal ADC step
T_s = 1 / f_s
Sample interval
STATE UNITS, REFERENCE, AND ASSUMPTIONS
Notes: Work one numerical or proportional example. Emphasize what changes, what remains fixed, and where the model stops being reliable.

## Slide 6
LECTURE 18 | PULSE MODULATION PCM ADCS AN
06
COMPARE BEFORE MEMORIZING
Reference model: ADC Resolution
Bits | Quantization Levels | Approximate Ideal SNR
4 | 16 | 25.8 dB
8 | 256 | 49.9 dB
10 | 1,024 | 62.0 dB
12 | 4,096 | 74.0 dB
16 | 65,536 | 98.1 dB
Notes: Use the table to compare cases and surface the tradeoff. Do not require memorization of implementation-specific numbers.

## Slide 7
LECTURE 18 | PULSE MODULATION PCM ADCS AN
07
EVIDENCE DISCIPLINE
Use a repeatable reasoning workflow
Observe
Model
Predict
Test
Qualify
Focus on representation accuracy and link behavior
Avoid code-heavy microcontroller discussion
DO NOT SKIP FROM A MEASUREMENT TO IDENTITY OR INTENT
Notes: The workflow is reusable: separate direct observation, model-based inference, and claims that require more evidence.

## Slide 8
LECTURE 18 | PULSE MODULATION PCM ADCS AN
08
APPLICATION, NOT REPLACEMENT
Cybersecurity follows the physical behavior
Digitization as a security boundary between analog truth and digital data
Resolution limits that hide small changes
DAC stair steps as observable metadata
Evidence boundary
State the tested condition and security consequence without claiming more than the measurement supports.
Notes: Keep the approximate 70/30 balance. Teach the communication mechanism first, then show how it changes availability, confidentiality, integrity, or authenticity.

## Slide 9
LECTURE 18 | PULSE MODULATION PCM ADCS AN
09
APPLY THE MODEL
Practice case
An 8-bit ADC covers 0-5 V. What does one code step represent, and what information is lost?
Given a sampling rate and input frequency, predict whether the sampled data represents the original signal or an alias.
Instructor key
One ideal step is about 19.5 mV; values within a step map to the same code.
Notes: One ideal step is about 19.5 mV; values within a step map to the same code. Ask for one alternate explanation and one measurement that would distinguish it.

## Slide 10
LECTURE 18 | PULSE MODULATION PCM ADCS AN
10
BRIDGE FORWARD
Exit check
What information is lost during sampling and quantization?
Answer with one model, one observable consequence, and one limit on the conclusion.
NEXT: ALIASING, FALSE TELEMETRY, AND SENSOR SPOO
Notes: Use the response to open the next meeting. Practice-case resolution: One ideal step is about 19.5 mV; values within a step map to the same code.