## Slide 1
LECTURE 10 | SYSTEMS + THREATS
01
CYBER 327 / LECTURE 10
Communication Blocks and Physical-Channel Threats
Locate signal failures before attributing cause, identity, or intent.
SEP 25, 2026
50-MINUTE SESSION
Notes: Zoom out from circuits to a complete communication system. Keep modulation and encoding at block-level preview; detailed analog modulation begins in Week 6.

## Slide 2
LECTURE 10 | SYSTEMS + THREATS
02
SYSTEM GOAL
Communication moves meaning through a physical channel
Message
Transmitter
Medium
Receiver
Recovered message
Every block transforms, transports, or interprets a physical signal.
Noise, interference, distortion, loss, and tamper can act before software receives data.
A VALID DIAGNOSIS LOCATES THE FAILURE IN THE CHAIN
Notes: Use a sensor-to-controller or access-point-to-client example. Ask students where Lab 4's filter belongs; accept transmitter or receiver front end with justification.

## Slide 3
LECTURE 10 | SYSTEMS + THREATS
03
CORE VOCABULARY
Message, signal, and carrier are not synonyms
Term | Meaning | Example
Message | Information to communicate | Temperature value or voice
Signal | Physical variation representing information | Voltage waveform or radio field
Carrier | Periodic waveform altered to transport a message | RF sine wave
Channel | Path and constraints between endpoints | Cable, air, or fiber
Notes: A baseband digital voltage can be a signal without using a separate sinusoidal carrier. Avoid saying every communication signal needs an RF carrier.

## Slide 4
LECTURE 10 | SYSTEMS + THREATS
04
BLOCK-LEVEL PREVIEW
Encoding and modulation solve different representation problems
Encoding
Maps information or bits into a defined representation.
Modulation
Changes a carrier property according to a message or symbol sequence.
Recovery
Detection, demodulation, decoding, and decisions reconstruct the message.
Notes: Do not teach AM/FM/PM math yet. Emphasize that these operations occur at purposeful blocks and can fail differently.

## Slide 5
LECTURE 10 | SYSTEMS + THREATS
05
CHANNEL CONSTRAINTS
The medium imposes a usable bandwidth
Copper, wireless, and optical paths attenuate and distort different frequencies differently.
Usable bandwidth is the range meeting a stated amplitude, phase, noise, or error criterion.
More signal bandwidth can carry faster changes, but occupies more channel resources.
Filtering outside the usable band cannot recover information the channel already destroyed.
Week 5 preview
Time-domain shape depends on frequency content; noise and SNR further limit reliable information rate.
Notes: Avoid fixed historical bandwidth memorization. Focus on criteria and tradeoffs.

## Slide 6
LECTURE 10 | SYSTEMS + THREATS
06
PLEX VOCABULARY
Direction and sharing describe different system behaviors
Mode | Direction | Example | Risk or constraint
Simplex | One way | Broadcast sensor | No return path for feedback
Half-duplex | Both ways, not simultaneously | Push-to-talk radio | Turn-taking and contention
Full-duplex | Both ways simultaneously | Telephone link | Isolation and self-interference
Multiplexed | Multiple users/signals share resources | Time or frequency slots | Coordination and separation
Notes: Multiplexing is not another direction mode. Keep it as resource sharing and defer techniques to later weeks.

## Slide 7
LECTURE 10 | SYSTEMS + THREATS
07
CAUSE VERSUS OBSERVATION
Noise, interference, and jamming require careful labels
Label | What it means | What measurement may show
Noise | Unwanted random or aggregate variation | Raised floor or uncertain samples
Interference | Unwanted energy that overlaps or affects reception | Tones, bursts, distortion, or errors
Jamming | Intentional interference intended to disrupt | Disruption evidence plus separate evidence of intent
Notes: A waveform or spectrum can establish interference but usually cannot establish intent. Use jamming only when intent is known from the controlled scenario or corroborating evidence.

## Slide 8
LECTURE 10 | SYSTEMS + THREATS
08
CYBERSECURITY CONNECTION
Physical threats map to security consequences
Physical event | Primary concern | Example evidence
Interference or cut path | Availability | Reduced output, link loss, errors
Unintended emission or tap | Confidentiality | Correlated recoverable signal
Component change or injected signal | Integrity | Response shift or altered decisions
Unknown transmitter | Authenticity | Requires more than energy detection
Notes: Security properties overlap. Require a stated asset and consequence rather than attaching a cyber label to every circuit anomaly.

## Slide 9
LECTURE 10 | SYSTEMS + THREATS
09
ASSET - PATH - CONSEQUENCE - CONTROL
Threat-model one physical path at a time
Asset
Exposure/path
Observable effect
Consequence
Control
Name what must remain available, confidential, accurate, or authentic.
State the physical access and capability required for the scenario.
Select a control and identify a measurement that would verify it.
DO NOT SKIP FROM ANOMALY TO ADVERSARY
Notes: Example: asset=5 kHz command channel; path=off-channel coupled tone; effect=reduced receiver output margin; consequence=availability loss; control=front-end selectivity plus monitoring.

## Slide 10
LECTURE 10 | SYSTEMS + THREATS
10
FILTER IN CONTEXT
Receiver selectivity protects a limited resource
Antenna or cable
Input protection
Band selection
Amplification
Detection
Early filtering can reduce out-of-band energy before sensitive stages overload.
The passband must still preserve the desired signal's occupied bandwidth and drift.
A FILTER IS ONE CONTROL, NOT A COMPLETE RECEIVER
Notes: Connect directly to Lab 4. The breadboard RLC path models one selective stage, not a complete secure receiver.

## Slide 11
LECTURE 10 | SYSTEMS + THREATS
11
DESIGN TRADEOFFS
A filter has limits an attacker or fault can expose
In-band energy
Passes through the same frequency region as the desired signal.
Overload
Strong energy may cause nonlinearity before or despite intended filtering.
Detuning
Tolerance, temperature, damage, or alteration shifts the response.
Notes: Do not imply the Lab 4 passive filter defeats a real jammer. It demonstrates one selective mechanism under safe wired conditions.

## Slide 12
LECTURE 10 | SYSTEMS + THREATS
12
OBSERVATION BEFORE INFERENCE
Case: the expected channel becomes weak
Step | Question | Useful measurement
Observe | What changed directly? | Input and output amplitude versus frequency
Localize | Transmitter, path, filter, or receiver? | Known input at each boundary
Hypothesize | Interference, loss, detuning, or instrument error? | Controlled A/B test
Verify | Did the control restore performance? | Repeated response and baseline comparison
Notes: A shifted response supports detuning. It does not distinguish drift, damage, or deliberate replacement without additional evidence.

## Slide 13
LECTURE 10 | SYSTEMS + THREATS
13
FRIDAY HANDOFF
Lab 4 turns filter response into message recovery
Measure RC high-pass and RL low-pass behavior first.
Combine the same parts into a series-RLC band-pass path.
Measure a response curve instead of trusting nominal labels.
Disconnect the generator and attach the verified wired audio source.
Recover a Morse-code carrier masked by out-of-band tones.
Evidence reminder
Preserve one RC/RL response, the final circuit, and the message-station input/output comparison.
Notes: Lab remains locked until component, audio-interface, speaker-loading, Morse-track, throughput, and timing validation pass. If it has not passed, restore the archived version or use checked fallback evidence.

## Slide 14
LECTURE 10 | SYSTEMS + THREATS
14
EXIT CHECK
Week 4 synthesis
A receiver input is healthy, but its desired-channel output is weak and its response peak has shifted.
Name one supported diagnosis, one security consequence, and one measurement needed next.
NEXT: SPECTRUM + SNR
Notes: Supported: the selective stage is detuned under the test. Consequence may be availability or integrity. Next: repeat, verify input, inspect components, compare baseline, or test the original resonance. Intent remains unsupported.