## Slide 1
LECTURE 03 | PARALLEL + POWER
01
CYBER 327 / LECTURE 03
Parallel Circuits and Loading
A new branch changes a lot
SEP 09, 2026

## Slide 2
LECTURE 03 | PARALLEL + POWER
02
OPENING CASE
What happens when you add a parallel load?
Before:
I = 5mA

## Slide 3
LECTURE 03 | PARALLEL + POWER
03
OPENING CASE
What happens when you add a parallel load?
Question
What must the source now provide, and what happens if it cannot?
Element | Voltage | Current | Power
R1 |  |  | 
R2 |  |  | 
Source |  |  | 
The load determines the requested current through Ohm’s law.
If the source reaches its current limit, its output voltage may fall.
Wiring and connection resistance can also produce voltage droop under load.

## Slide 4
LECTURE 03 | PARALLEL + POWER
02
OPENING CASE
Battery Load Testing

## Slide 5
LECTURE 03 | PARALLEL + POWER
02
OPENING CASE
Ampacity
700 A
3 A
0.75 A
The maximum safe current for a component under certain conditions.
stored charge, normally measured in Ah or mAh.
Battery Capacity

## Slide 6
LECTURE 03 | PARALLEL + POWER
02
OPENING CASE
What happens when you add sources?
SERIES
Voltages add
Current is limited by weakest source
PARALLEL
Same voltage, more current
NEVER PARALLEL DIFFERENT SOURCES

## Slide 7
LECTURE 03 | PARALLEL + POWER
04
PARALLEL RESISTANCE
Equivalent resistance
Every added parallel path lowers equivalent resistance.
A shortcut

## Slide 8
LECTURE 03 | PARALLEL + POWER
04
PARALLEL RESISTANCE
Conductance
The reciprocal of resistance
Units: Siemens (S)
1 Ω = 1 S
1 kΩ = 1 mS
1 MΩ = 1 µS
GT = G1 + G2

## Slide 9
LECTURE 03 | PARALLEL + POWER
08
WORKED MEASUREMENT
Loading Effects
After adding voltmeter:
THE INSTRUMENT BECOMES PART OF THE CIRCUIT
Before adding voltmeter:

## Slide 10
LECTURE 03 | PARALLEL + POWER
11
EVIDENCE DISCIPLINE
Observation is not inference
Observation
A directly measured, repeatable fact. Example: the rail is 5.0 V with Load A alone and 4.6 V when Load B is enabled.
Inference
A limited conclusion supported by that evidence. Example: the source or shared path cannot maintain 5.0 V at the combined load.
Not Yet Known
The exact failed component, cause, or intent. Choose another controlled measurement before claiming more.

## Slide 11
LECTURE 03 | PARALLEL + POWER
12
CLAIM - EVIDENCE - NEXT TEST
Case: a shared rail drops from 5.0 V to 4.6 V
Observed
Voltage is correct with Load A alone and falls when Load B is enabled.
Supported
The source or shared path cannot maintain 5.0 V at the combined load.
Next test
Measure each branch current and source voltage at the terminals under controlled states.
Notes: Alternatives include current limit, weak supply, wiring resistance, incorrect Load B, or short. Do not jump directly to malicious load.

## Slide 12
LECTURE 03 | PARALLEL + POWER
12
TAKEAWAYS
Circuits Summary
Property | Series | Parallel
All elements have the same |  | 
Largest R has | Largest/Smallest V Largest/Smallest P | Largest/Smallest I Largest/Smallest P
Rtotal is: | Greater/Less than Rmax | Greater/Less than Rmin
When there is a broken element: |  | 

## Slide 13
LECTURE 03 | PARALLEL + POWER
12
CLAIM - EVIDENCE - NEXT TEST
Circuits Summary
Property | Series | Parallel
All elements have the same | I | V
Largest R has | Largest/Smallest V Largest/Smallest P | Largest/Smallest I Largest/Smallest P
Rtotal is: | Greater/Less than Rmax | Greater/Less than Rmin
When there is a broken element: | Open circuit | No effect

## Slide 14
LECTURE 03 | PARALLEL + POWER
13
BEFORE FRIDAY
Exit check
NEXT: INSTRUMENTS + AC WAVEFORMS