## Slide 1
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
01
CYBER 327 / LECTURE 11
Time Domain, Frequency Domain, Fourier, and Harmonics
The same waveform tells different stories in time and frequency.
MONDAY, SEPTEMBER 28, 2026
\
Notes: \

## Slide 2
LECTURE 10 | SYSTEMS + THREATS
02
RECALL
The Communication System
Message
Transmitter
Medium
Receiver
Recovered message
Signal
Encoding Method
Wire (copper)
Wireless
Optical Fiber
Interference
Noise

## Slide 3
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
02
STARTING CONCEPTS
From Time to Frequency Domain
James Fourier
What if signals can be expressed as a sum of fundamental sinusoids?
Notes: First question: how does heat spread through an object?
Fourier Series
Fourier Transform

## Slide 4
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
02
STARTING CONCEPTS
The Fourier Transform
Time Domain
What is the signal doing over time?
Frequency Domain
What frequencies make up the signal?
Demo
Notes: First question: how does heat spread through an object?
Fourier Series
Fourier Transform

## Slide 5
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
02
STARTING CONCEPTS
The Fourier Transform
Time Domain
What is the signal doing over time?
Frequency Domain
What frequencies make up the signal?
Demo
Notes: First question: how does heat spread through an object?
Fourier Series
Fourier Transform

## Slide 6
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
04
QUANTITATIVE MODEL
Core ideas
Term | Meaning
time domain | View of signal amplitude as a function of time.
frequency domain | View of how signal energy or amplitude is distributed across frequency.
Period and frequency
Recall: Filters

## Slide 7
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
06
COMPARE BEFORE MEMORIZING
Harmonics
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle | Odd: 1, 3, 5, 7, 9 … [ decay] | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle |  | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Harmonic locations
fundamental
The lowest-frequency periodic component associated with a repeating waveform.
harmonic
the extra sine waves that combine to give a waveform its shape.

## Slide 8
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
06
COMPARE BEFORE MEMORIZING
Harmonics
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle | Odd: 1, 3, 5, 7, 9 … [ decay] | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle |  | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Harmonic locations
fundamental
The lowest-frequency periodic component associated with a repeating waveform.
harmonic
A frequency that is a whole-number multiple of the fundamental frequency

## Slide 9
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
06
COMPARE BEFORE MEMORIZING
Harmonics
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle | Odd: 1, 3, 5, 7, 9 … [ decay] | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle |  | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Harmonic locations
fundamental
The lowest-frequency periodic component associated with a repeating waveform.
Rapid changes in time require more high-frequency content.
Demo

## Slide 10
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
06
COMPARE BEFORE MEMORIZING
Harmonics
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle | Odd: 1, 3, 5, 7, 9 … [ decay] | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle |  | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Harmonic locations
fundamental
The lowest-frequency periodic component associated with a repeating waveform.
Rapid changes in time require more high-frequency content.
Demo

## Slide 11
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
06
COMPARE BEFORE MEMORIZING
Harmonics
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle | Odd: 1, 3, 5, 7, 9 … [ decay] | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Waveform | Dominant spectral pattern | Relative Bandwidth
Sine | One ideal tone (fundamental only) | Narrowest
Triangle |  | Low
Square | Odd: 1, 3, 5, 7, 9 ... | Intermediate
Sawtooth | All: 1, 2, 3, 4, 5, 6 … | High
Pulse | Many harmonics set by width | All
Harmonic locations
fundamental
The lowest-frequency periodic component associated with a repeating waveform.
Rapid changes in time require more high-frequency content.
Demo

## Slide 12
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
08
APPLICATION, NOT REPLACEMENT
Cybersecurity follows the physical behavior
Spectral fingerprints for signal identification
Detectability from amplitude, bandwidth, harmonics, and duty cycle
What does the time-domain representation of a periodic waveform tell you about its BW requirements?
Why do instruments and waveforms all sound different if they are at the same frequency?
What single periodic waveform has a single frequency component?
What periodic waveform do we always use as the carrier in electronic communication?
What is a harmonic?
What happens to a sine wave’s spectrum when we change its amplitude over time to carry information?
Review
Notes: The sharper and faster the waveform changes, the more high-frequency harmonics it needs → more bandwidth. A smooth sine wave needs very little BW; sharp pulses need much more.
They can have the same fundamental frequency (pitch) but different harmonics. Different harmonic content gives them different timbre or sound quality.
A sine wave. An ideal sine wave contains only one frequency.
A sinusoidal carrier (sine/cosine). A pure sinusoid provides a single, well-defined carrier frequency.
A frequency that is a whole-number multiple of the fundamental frequency. For a 1 kHz fundamental, 2 kHz is the 2nd harmonic, 3 kHz the 3rd, etc.
If we start changing the sine wave to carry information, additional frequency components appear around the original frequency.

## Slide 13
LECTURE 11 | TIME DOMAIN FREQUENCY DOMAIN
10
BRIDGE FORWARD
Exit check
What features distinguish a square wave from a sine wave in the spectrum?
NEXT: DECIBELS, NOISE, SNR, AND SHANNON CAPACITY