## Slide 1
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
01
CYBER 327 / LECTURE 25
Line Coding, Pulse Impairments, and Eye Patterns
The bits are correct. Will the wire and sampling clock preserve them?
FRIDAY, OCTOBER 30, 2026
Notes: Bridge: Lecture 22 mapped bits to signal states; Lecture 23 measured recovery; Lecture 24 organized carriers and dealt with delayed paths. Today inspect actual pulses and the sampling decision. A connection may pass a continuity check yet fail to deliver bits at the required rate. No new live demonstration is required.

## Slide 2
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
02
FOLLOW THE COMMUNICATION CHAIN
A receiver needs the right level at the right time
Bits
Line code
Channel
Sample
Check
Line coding chooses physical levels or transitions; the channel changes their shape.
Error-control coding and encryption perform separate jobs.
Notes: Follow message bits through a line encoder, channel, receiver sampling and frame checks. Line coding chooses physical levels/transitions. Error-control coding adds redundancy for detection/correction; encryption addresses privacy. These are separate jobs. Carrier-based QAM and wired line coding are different representations, while both require usable waveforms and timing. Do not claim the DC-08 serial interface uses the specific example codes on later slides.

## Slide 3
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
03
A TRANSITION HAPPENS AT THE START OF A BIT INTERVAL; CONVENTIONS MUST BE STATED
NRZ: agree on levels or changes
Code / full name | Our rule | Needed agreement
NRZ-L: non-return-to-zero level | 1 = high; 0 = low | Polarity and bit timing
NRZ-M: non-return-to-zero mark | 1 = change; 0 = hold | Initial level and bit timing
NRZ-S: non-return-to-zero space | 0 = change; 1 = hold | Initial level and bit timing
Notes: Define NRZ as non-return-to-zero: no mandatory neutral return inside each bit. L means level, M means mark (one), S means space (zero). Declare the convention: NRZ-L high=1/low=0; NRZ-M changes at a bit boundary for 1; NRZ-S changes for 0. For M/S, start low immediately BEFORE the first interval. Both ends need the same rule and starting-state/timing information. The name NRZI can be used with different transition conventions; do not infer it without checking.

## Slide 4
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
04
DECLARED CONVENTIONS; HIGH IS NOT ALWAYS A DATA ONE
Encode the same 1 0 1 1 0 0 0 1 message
1
0
1
1
0
0
0
1
NRZ-L
NRZ-M
NRZ-S
NRZ-M / NRZ-S start LOW immediately before the first bit. Same message; different representations.
Notes: Use the same bits as Lecture 22/23: 10110001. Ask students to predict each waveform before tracing it. NRZ-L: H L H H L L L H. NRZ-M from initial low: H H L H H H H L. NRZ-S: L H H H L H L L. A high level is not automatically bit 1 in a transition code. Vertical guides are bit boundaries, not additional transmitted clock pulses.

## Slide 5
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
05
PRACTICE BEFORE VIEWING THE SPEAKER-NOTE ANSWERS
Decode changes, not just high and low
NRZ-M; initial level LOW. Compare each level with the previous one.
Received levels, one per bit | What do you recover?
H H L H H H H L | Write 1 for a change; 0 for no change.
Use NRZ-S on the same levels | Does the decoded message stay the same?
Notes: Pause 45 seconds before revealing the notes answer. Starting low, compare each level with the previous one. Change/no-change pattern is 1 0 1 1 0 0 0 1. Therefore recover 10110001. Under NRZ-S the same level history would decode 01001110. Starting state also affects the first decision. Incorrect configuration can produce repeatable wrong bits without channel noise.

## Slide 6
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
06
MANCHESTER HAS A MIDPOINT TRANSITION; AMI = ALTERNATE MARK INVERSION
Other codes arrange transitions differently
1
0
1
1
0
0
Manchester
AMI
Manchester: 1 rises and 0 falls at mid-bit. AMI: zero is neutral; successive ones alternate + / -. First mark is positive.
Notes: Manchester convention here: 1 is low-to-high in the middle of the bit; 0 is high-to-low. The midpoint transition is mandatory; bit-boundary transitions may also occur. AMI means alternate mark inversion: zero uses the neutral level, successive ones alternate positive and negative pulses. Declare first mark positive. These are schematic polar/three-level examples, not connector voltage specifications. AMI was important in telephone digital links; keep history brief. Alternating marks reduce DC content, but long zero runs still lack transitions.

## Slide 7
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
07
CLOCK RECOVERY ESTIMATES WHEN TO SAMPLE; A LINE CODE DOES NOT AUTHENTICATE THE SENDER
Timing information has a physical cost
Code | Run with few / no transitions | Tradeoff
NRZ-L | Long run of the same bit | Clock recovery needs other provisions
NRZ-M / NRZ-S | Zeros for M / ones for S | Transition rule does not guarantee an edge in every bit
Manchester | Every bit has a midpoint transition | Faster level intervals; generally more bandwidth
AMI | Long zero run is neutral | Alternating marks reduce DC; zeros still need timing support
Notes: Clock recovery means estimating where bit intervals begin and where to sample, not just guessing a voltage threshold. NRZ-L long constant runs give no edges. NRZ-M zeros and NRZ-S ones give no boundary transitions. Manchester guarantees a midpoint transition but uses faster level intervals and generally requires more bandwidth for comparable pulse shaping. AMI zeros still lack transitions. Modern systems can add framing, scrambling or other timing provisions; no code provides authentication automatically.

## Slide 8
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
08
T_S = 1 / R_S COUNTS SYMBOLS; T_B = 1 / R_B COUNTS BITS
A faster edge pattern is not more message bits
Bit duration: T_b = 1 / R_b. Given R_b = 100 kbit/s.
Representation | Time calculation | New message rate
Binary NRZ bit interval | 1 / 100,000 = 10 us | 100 kbit/s
Manchester half-bit interval | 10 us / 2 = 5 us | Still 100 kbit/s
Notes: At 100 kbit/s, Tb=1/100000=10 us. Binary NRZ uses one level interval per bit here. Manchester's half-bit interval is 5 us, but its message rate remains 100 kbit/s. Do not report 200 kbit/s of new information. Ts=1/Rs counts symbols; Tb=1/Rb counts bits. They coincide for one-bit-per-symbol binary NRZ, not for QPSK where a symbol represents two mapped bits. No universal exact bandwidth formula is inferred just from these sketches.

## Slide 9
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
09
CONNECT FINITE BANDWIDTH TO THE HARMONICS IN LECTURE 11
Real channels change the pulse shape
Idealized pulses
Bandwidth-limited edges
Added voltage variation
Overshoot and ringing
Constructed examples. Appearance suggests tests; it does not uniquely identify a cause.
Notes: Identify the visual changes before proposing a cause: rounded edges, added voltage variation, or overshoot/ringing. Finite channel bandwidth limits edge speed; filtering can also remove noise, so the design needs an appropriate bandwidth rather than arbitrarily maximum bandwidth. Ringing can arise from channel/termination effects. These are constructed waveforms, not measurements or unique diagnoses. Link sharp transitions back to Lecture 11's harmonics.

## Slide 10
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
10
CONSTRUCTED PATTERN-HISTORY EXAMPLE; THE SAME CURRENT ZERO CAN SAMPLE DIFFERENTLY
A previous bit can change the current decision
ISI = intersymbol interference. Nominal 0 / 1 V; threshold = 0.5 V.
Previous bit | Current bit sent | Sampled voltage | Decision
0 | 0 | 0.1 V | 0: correct
0 | 1 | 0.9 V | 1: correct
1 | 0 | 0.6 V | 1: wrong
Notes: ISI means intersymbol interference: energy from one symbol affects a neighboring symbol's decision. The toy observations isolate pattern history, not a fitted channel model. Nominal levels are 0/1 V, threshold 0.5 V. A current zero after zero measures 0.1 V and decodes correctly. A current zero after one measures 0.6 V and is misread as one. The receiver sees the same intended current bit but a different sampled voltage because of history. It is not necessarily a random voltage-noise problem.

## Slide 11
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
11
IMPEDANCE DISCONTINUITIES CAN REFLECT PART OF A TRAVELING SIGNAL
A mismatch can add an unwanted echo
Reference connection
Driver
Receiver
Cable / transmission path
Added branch / changed termination
Driver
Receiver
Cable / transmission path
Branch / discontinuity
Some energy reflects: a delayed copy can distort later pulses.
Effect depends on edge speed, impedances and delay. DC continuity alone does not test these effects.
Notes: Impedance mismatch means an abrupt difference from the impedance the traveling waveform expects. Some signal energy reflects, and a delayed copy can add to a later part of the waveform. An extra cable branch or unsuitable termination may cause this. The amount depends on the actual channel, impedances, edge speed and delays; do not claim every branch always fails. A DC continuity test cannot characterize these fast effects. Further transmission-line analysis comes later in the course.

## Slide 12
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
12
A TIME-DOMAIN DISPLAY, NOT A CONSTELLATION OR FREQUENCY SPECTRUM
Build an eye by overlaying aligned windows
1. Align
Use the symbol timing reference.
2. Cut
Take equal time windows.
3. Overlay
Overlay windows on identical axes.
H
L
0
0.5
1 UI
Many bit histories, one timing reference
UI = unit interval. The overlay summarizes decision conditions; it is not a readable message.
Notes: An eye overlays many waveform segments aligned to symbol timing. Here show one-unit-interval windows with a little surrounding time; UI means unit interval, one symbol period in the selected display. Different bit histories create different traces. An overlay summarizes decision conditions, not a readable copy of the message. Do not promise that an ordinary scope has an automatic eye mode; the same idea can be shown in software or prepared captures. The figures are deterministic teaching sketches.

## Slide 13
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
13
USE STATED SAMPLE TIMING, THRESHOLD AND MEASUREMENT CRITERIA
An open eye leaves voltage and timing room
H
L
0
0.5
1 UI
Height: voltage opening
At the stated sampling instant: how far apart are the observed level bands?
Width: timing window
At the stated decision criterion: when can you sample with margin?
Conceptual opening only. Record the measurement definition, scales, clock reference and sample count.
Notes: At a stated sampling instant, vertical separation between upper/lower observed bands gives a voltage opening. At a stated decision criterion, horizontal opening gives a usable timing window. Choose a threshold between bands and sample away from transitions; the center is a sensible choice for this symmetric illustration, not a universal calibrated optimum. Eye height is not the margin to EACH side of a threshold. Actual instrument definitions may use statistical levels/BER contours, unlike these simple observed-bound examples.

## Slide 14
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
14
TIMING JITTER = TRANSITION-TIME VARIATION RELATIVE TO A REFERENCE
Look at which direction the eye closes
Open reference
H
L
0
0.5
1 UI
Clear voltage and timing separation
Voltage variation
H
L
0
0.5
1 UI
Mainly reduces vertical separation
Transition jitter
H
L
0
0.5
1 UI
Mainly reduces horizontal opening
Same scales; schematic examples. ISI and mixed impairments can reduce both openings.
Notes: Compare patterns, not supposed attacker signatures. The noise sketch spreads traces mainly vertically; the jitter sketch shifts transitions mainly horizontally. Jitter is variation in transition timing relative to a reference. Bandwidth limitation and ISI can close both dimensions. Mixed causes are common. Keep vertical/time scales, sample count, clock-reference method and measurement point comparable. Eye appearance alone does not uniquely establish the impairment or the BER.

## Slide 15
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
15
MARGINS DESCRIBE SUPPLIED OBSERVATIONS; THEY DO NOT PREDICT AN EXACT BER
Eye height and threshold margin are different
Observed bounds; threshold = 0.5 V; bit duration = 10 us.
Given / quantity | Calculation | Result
Low maximum 0.2 V; high minimum 0.8 V | 0.8 - 0.2 | 0.6 V eye height
Threshold margin, smaller side | min(0.8 - 0.5, 0.5 - 0.2) | 0.3 V voltage margin
Usable sampling window 2-8 us | Center = 5 us; min(5 - 2, 8 - 5) | 3 us timing margin
Notes: Work the supplied observed bounds. High minimum 0.8 V minus low maximum 0.2 V gives eye height 0.6 V. With threshold 0.5 V, each side has 0.3 V margin; use the smaller side if asymmetric. A usable 2-8 us window is 6 us wide; sample at 5 us for 3 us margin to either edge. With Tb=10 us these are inside one bit. The criteria and finite record are supplied; no lifetime error-free guarantee or BER calculation follows from these gaps alone.

## Slide 16
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
16
AN EYE SUGGESTS A TEST; A REPEATABLE TEST SUPPORTS A CONCLUSION
Diagnose with a controlled comparison
Reference
Verify setup
Change one
Restore
Compare
Check code convention, bit rate, sampling, loading and instrument bandwidth.
Use known reference bits for BER; preserve settings and compared-bit count.
Notes: Use a known bit reference, not unknown application traffic, to count BER. Verify code convention, bit rate, timing/threshold, probe/cable loading and instrument bandwidth before blaming the link. Compare against a saved baseline, change one parameter, restore it and recheck. Capture the eye and error count/compared-bit count at a stated receiver point. Recovery after a controlled change supports a causal hypothesis, but multiple changes at once do not isolate the cause.

## Slide 17
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
17
SEPARATE SIGNAL INTEGRITY FROM SECURITY CHECKS
A changed cable can disrupt a security system
Observation / event | Possible consequence | What is still unknown?
Tap, branch or cable replacement | Reflections or distorted pulses | Whether this change caused the observed failure
Legitimate command fails or times out | Availability is reduced | Accident, configuration error or deliberate interference?
Clean reception after link repair | Bits arrive more reliably | Sender authorization, freshness and permission
Notes: Scenario: a maintenance tap or cable replacement adds an unintended branch. Pulse distortion makes a legitimate door command fail its check or timeout. This is an availability risk. The waveform alone cannot distinguish an authorized but poor installation from sabotage. Encryption does not restore distorted pulse decisions; link repair and sender authentication/freshness solve separate problems. Do not portray every tap as causing errors or every impedance change as evidence of an attacker.

## Slide 18
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
18
LAB 9 IS A PLANNED SIMULATION/CAPTURE ACTIVITY; ITS IMPLEMENTATION STILL NEEDS VALIDATION
Use the right display for the question
Evidence | What it shows | Connection to planned Lab 9
Constellation | I/Q symbol positions | QPSK versus 16-QAM decision spacing
Eye | Time-domain component levels and timing | I/Q eyes can have multiple vertical openings
Spectrum | Power across frequency | Occupied span and filtering
BER: bit error rate | Wrong bits / aligned compared bits | Choose a candidate meeting rate and error limits
Notes: Connect the week's four displays: constellation is I/Q position, spectrum is power versus frequency, eye is a time-domain overlay, BER compares recovered bits with an aligned known reference. In QAM a component eye may have multiple vertical openings: a four-level I or Q component of square 16-QAM has three, while two-level QPSK components have one. Planned Lab 9 compares QPSK/16-QAM with controlled impairments and a rate/BER target. It remains a paper plan pending a working simulator/captures and validation; do not announce a ready live lab. No RF transmitter or Arduino is required by that plan.

## Slide 19
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
19
STATE THE CONVENTION, STARTING LEVEL, UNITS AND LIMITS OF THE CONCLUSION
Practice: decode, then check the margins
Decode the bits; calculate bit duration and observed decision margins.
Given | Find
NRZ-M; initial LOW; H L L L H H | Recovered bits
Message rate 200 kbit/s | Bit duration
Low max 0.3 V; high min 0.9 V; threshold 0.6 V | Eye height and worst voltage margin
Usable sampling window 1-4 us | Center and timing margin
Notes: Allow about two minutes for individual work or pairs. NRZ-M initial low, levels H L L L H H -> 110010. Rb=200 kbit/s -> Tb=5 us. Eye height 0.9-0.3=0.6 V; threshold 0.6 gives 0.3 V worst voltage margin. Usable time window 1-4 us gives center 2.5 us and 1.5 us margin to either boundary. Ask one student to explain why a correct code rule alone does not guarantee a correct sampled voltage. Do not use these supplied ranges to claim a numerical BER.

## Slide 20
LECTURE 25 | LINE CODING PULSE IMPAIRMENT
20
CHECK UNDERSTANDING
Explain the next step
The eye closes. What can you conclude?
Name the lost decision margin, one controlled test, and one claim the display does not establish.
NEXT: MEDIA, TIMING AND COMPRESSION
Notes: Expected exit response: less voltage separation/timing window under the displayed measurement conditions; investigate code/settings, channel bandwidth, noise, jitter or reflections with a controlled comparison. No unique cause, attacker identity or sender authorization follows from the eye alone. Next lecture applies rate, error and timing limits to media delivery, including video, buffering and compression. No script file was requested or produced for this revision.